AVR001: USB communication initialized by touch-switch

# Control messages
Control messages that are being sent by USB host to AVR device are:
- REQ_GET_HEADER, requesting devices's header that is going to be specific for each AVR device indivitually (i.e. AVR001 device will have hex header of 0x01, etc.).
- REQ_GET_DATA1, a state of the touch-switch
- REQ_GET_DATA2, a clock interval; default value should be 5 secs.
- REQ_GET_DATA3, threshold value; any request from host with request value being greater from REQ_GET_DATA3 is going to be threaded as offset value that will 1-1 map to “memory counter” value, an index of sent data.

# AVRDUDE guidelines
Default fuse values for Attiny85 are:
LFUSE = 0x62
HFUSE = 0xDF
EFUSE = 0xFF
For external xtal clock, based upon http://www.engbedded.com/fusecalc/, LFUSE should be set to 0x6F.